## Slide 1: Arduino Uno
A microcontroller brain for your electronics projects: pins, functions and the voltage divider
Notes: Introduction to the Arduino Uno: what it is, how its pins work, and how a voltage divider is built and calculated (SCRUM-25).

## Slide 2: What is the Arduino Uno?
A digital microcontroller that can be used as the brain of an electronics project. It has both analog and digital pins.
ATmega328P
8-bit CMOS chip that forms the CPU
Analog + Digital
Two kinds of pins on one board
Notes: The Uno is built around an ATmega328P, an 8-bit CMOS chip that acts as the CPU. It exposes analog and digital pins.

## Slide 3: Digital and analog pins
Figure 1: Arduino Uno pins
Digital pins
Marked DIGITAL on the board
Analog pins
Marked ANALOG IN (A0 to A5)
Notes: Digital and analog pins read and execute differently. Figure 1 shows where each group sits on the board.

## Slide 4: Declare a pin before using it
To read any pin value, the pin must first be declared in void setup() as either INPUT or OUTPUT.
void setup() {
pinMode(pin, INPUT);
pinMode(pin, OUTPUT);
}
INPUT
Read a value from the pin
OUTPUT
Send a command out of the pin
Notes: pinMode is called inside void setup() for every pin you plan to use.

## Slide 5: Reading and writing pins
DIGITAL PINS
Read with
digitalRead(pin)
Write / execute with
digitalWrite(pin, value)
ANALOG PINS
Read with
analogRead(pin)
Write with
analogWrite(pin, value)
Notes: Digital pins use digitalRead and digitalWrite; analog pins use analogRead and analogWrite.

## Slide 6: The voltage divider circuit
Figure 2: Voltage divider circuit
5.00 V
Voltage in
3.33 V
Voltage out
1.67 mA
Current
Notes: Two resistors in series across a 5 V supply. The multimeter between them reads 3.33 V.

## Slide 7: The voltage divider formula
Vout = R2 / (R1 + R2) × Vin
Worked example (Figures 2 and 3)
3.333 V = 2 / (2 + 1) × 5 V
R2 is the resistor the output is measured across; R1 sits between the supply and the output.
Notes: Vout = R2 / (R1 + R2) x Vin. With R1 = 1 and R2 = 2 and 5 V in, the output is 3.333 V.